## Slide 1: Ponavljanje

## Slide 2
https://people.vts.su.ac.rs/~pmiki/_DALJINSKA_NASTAVA_MIKROKONTROLERI/03.06/VUpotmet.mp4

## Slide 3: VU metar potenciometar
const int led1 = 2;
const int led2 = 3;
const int led3 = 4;
const int led4 = 5;
const int led5 = 6;
const int led6 = 7;
const int led7 = 8;
const int led8 = 9;
const int potPin = A0;
int potValue;
void setup(){
Serial.begin(9600);
for (int i=2; i<10; i++){
pinMode(i, OUTPUT);
}
pinMode(potPin, INPUT);
}
void loop(){
potValue = analogRead(potPin);
Serial.print("Pot meter value: ");
Serial.println(potValue);
if (potValue>0 && potValue<128){
digitalWrite(led1, HIGH);
digitalWrite(led2, LOW);
digitalWrite(led3, LOW);
digitalWrite(led4, LOW);
digitalWrite(led5, LOW);
digitalWrite(led6, LOW);
digitalWrite(led7, LOW);
digitalWrite(led8, LOW);
}

## Slide 4: VU metar potenciometar
if (potValue>127 && potValue<256){
digitalWrite(led1, HIGH);
digitalWrite(led2, HIGH);
digitalWrite(led3, LOW);
digitalWrite(led4, LOW);
digitalWrite(led5, LOW);
digitalWrite(led6, LOW);
digitalWrite(led7, LOW);
digitalWrite(led8, LOW);
}
if (potValue>255 && potValue<384){
digitalWrite(led1, HIGH);
digitalWrite(led2, HIGH);
digitalWrite(led3, HIGH);
digitalWrite(led4, LOW);
digitalWrite(led5, LOW);
digitalWrite(led6, LOW);
digitalWrite(led7, LOW);
digitalWrite(led8, LOW);
}
if (potValue>383 && potValue<512){
digitalWrite(led1, HIGH);
digitalWrite(led2, HIGH);
digitalWrite(led3, HIGH);
digitalWrite(led4, HIGH);
digitalWrite(led5, LOW);
digitalWrite(led6, LOW);
digitalWrite(led7, LOW);
digitalWrite(led8, LOW);
}
if (potValue>511 && potValue<638){
digitalWrite(led1, HIGH);
digitalWrite(led2, HIGH);
digitalWrite(led3, HIGH);
digitalWrite(led4, HIGH);
digitalWrite(led5, HIGH);
digitalWrite(led6, LOW);
digitalWrite(led7, LOW);
digitalWrite(led8, LOW);
}

## Slide 5: VU metar potenciometar
if (potValue>639 && potValue<768){
digitalWrite(led1, HIGH);
digitalWrite(led2, HIGH);
digitalWrite(led3, HIGH);
digitalWrite(led4, HIGH);
digitalWrite(led5, HIGH);
digitalWrite(led6, HIGH);
digitalWrite(led7, LOW);
digitalWrite(led8, LOW);
}
if (potValue>767 && potValue<896){
digitalWrite(led1, HIGH);
digitalWrite(led2, HIGH);
digitalWrite(led3, HIGH);
digitalWrite(led4, HIGH);
digitalWrite(led5, HIGH);
digitalWrite(led6, HIGH);
digitalWrite(led7, HIGH);
digitalWrite(led8, LOW);
}
if (potValue>895 && potValue<1024){
digitalWrite(led1, HIGH);
digitalWrite(led2, HIGH);
digitalWrite(led3, HIGH);
digitalWrite(led4, HIGH);
digitalWrite(led5, HIGH);
digitalWrite(led6, HIGH);
digitalWrite(led7, HIGH);
digitalWrite(led8, HIGH);
}
delay(100);
}

## Slide 6
https://people.vts.su.ac.rs/~pmiki/_DALJINSKA_NASTAVA_MIKROKONTROLERI/03.06/VUjoystick.mp4

## Slide 7: VU metar joystick
const int led1 = 2;
const int led2 = 3;
const int led3 = 4;
const int led4 = 5;
const int led5 = 6;
const int led6 = 7;
const int led7 = 8;
const int led8 = 9;
const int X_pin = A5;
int joystickValue;
void setup(){
Serial.begin(9600);
for (int i=2; i<10; i++){
pinMode(i, OUTPUT);
}
pinMode(X_pin, INPUT);
}
void loop(){
joystickValue = analogRead(X_pin);
Serial.print("Joystick X value: ");
Serial.println(joystickValue);
if (joystickValue>0 && joystickValue<128){
digitalWrite(led1, HIGH);
digitalWrite(led2, LOW);
digitalWrite(led3, LOW);
digitalWrite(led4, LOW);
digitalWrite(led5, LOW);
digitalWrite(led6, LOW);
digitalWrite(led7, LOW);
digitalWrite(led8, LOW);
}

## Slide 8: VU metar joystick
if (joystickValue>127 && joystickValue<256){
digitalWrite(led1, HIGH);
digitalWrite(led2, HIGH);
digitalWrite(led3, LOW);
digitalWrite(led4, LOW);
digitalWrite(led5, LOW);
digitalWrite(led6, LOW);
digitalWrite(led7, LOW);
digitalWrite(led8, LOW);
}
if (joystickValue>255 && joystickValue<384){
digitalWrite(led1, HIGH);
digitalWrite(led2, HIGH);
digitalWrite(led3, HIGH);
digitalWrite(led4, LOW);
digitalWrite(led5, LOW);
digitalWrite(led6, LOW);
digitalWrite(led7, LOW);
digitalWrite(led8, LOW);
}
if (joystickValue>383 && joystickValue<512){
digitalWrite(led1, HIGH);
digitalWrite(led2, HIGH);
digitalWrite(led3, HIGH);
digitalWrite(led4, HIGH);
digitalWrite(led5, LOW);
digitalWrite(led6, LOW);
digitalWrite(led7, LOW);
digitalWrite(led8, LOW);
}
if (joystickValue>511 && joystickValue<638){
digitalWrite(led1, HIGH);
digitalWrite(led2, HIGH);
digitalWrite(led3, HIGH);
digitalWrite(led4, HIGH);
digitalWrite(led5, HIGH);
digitalWrite(led6, LOW);
digitalWrite(led7, LOW);
digitalWrite(led8, LOW);
}

## Slide 9: VU metar joystick
if (joystickValue>891 && joystickValue<1024){
digitalWrite(led1, HIGH);
digitalWrite(led2, HIGH);
digitalWrite(led3, HIGH);
digitalWrite(led4, HIGH);
digitalWrite(led5, HIGH);
digitalWrite(led6, HIGH);
digitalWrite(led7, HIGH);
digitalWrite(led8, HIGH);
}
delay(100);
}
if (joystickValue>639 && joystickValue<768){
digitalWrite(led1, HIGH);
digitalWrite(led2, HIGH);
digitalWrite(led3, HIGH);
digitalWrite(led4, HIGH);
digitalWrite(led5, HIGH);
digitalWrite(led6, HIGH);
digitalWrite(led7, LOW);
digitalWrite(led8, LOW);
}
if (joystickValue>767 && joystickValue<896){
digitalWrite(led1, HIGH);
digitalWrite(led2, HIGH);
digitalWrite(led3, HIGH);
digitalWrite(led4, HIGH);
digitalWrite(led5, HIGH);
digitalWrite(led6, HIGH);
digitalWrite(led7, HIGH);
digitalWrite(led8, LOW);
}

## Slide 10: Servo radar
https://people.vts.su.ac.rs/~pmiki/_DALJINSKA_NASTAVA_MIKROKONTROLERI/03.06/ServoRadarFail.mp4
https://people.vts.su.ac.rs/~pmiki/_DALJINSKA_NASTAVA_MIKROKONTROLERI/03.06/Ultra01.mp4
https://people.vts.su.ac.rs/~pmiki/_DALJINSKA_NASTAVA_MIKROKONTROLERI/03.06/Ultra02.mp4
https://people.vts.su.ac.rs/~pmiki/_DALJINSKA_NASTAVA_MIKROKONTROLERI/03.06/Ultra03.mp4

## Slide 12: Servo radar
#include <Servo.h>
Servo myServo;
int angle;
void setup() {
Serial.begin(9600);
myServo.attach(9);
}
void loop() {
for (angle=0; angle<180; angle++){
myServo.write(angle);
delay(25);
}
for (angle=179; angle>0; angle--){
myServo.write(angle);
delay(25);
}
}

## Slide 13: Ultrazvučni senzor

## Slide 14: Ultrazvučni senzor
#define echo 11 // Echo Pin
#define trig 12 // Trigger Pin
long travel_time, distance; // Duration used to calculate distance
int shortestDistance=10000;
void setup() {
Serial.begin (9600);
pinMode(trig, OUTPUT);
pinMode(echo, INPUT);
}

## Slide 15: Ultrazvučni senzor
void loop() {
digitalWrite(trig, LOW);
delayMicroseconds(2);
//Sending a high pulse to trigger the //Ultrasound Module
digitalWrite(trig, HIGH);
delayMicroseconds(10);
digitalWrite(trig, LOW);
travel_time = pulseIn(echo, HIGH);
//Calculating the distance
distance = (travel_time*0.034)/2;
if (distance<shortestDistance){
shortestDistance = distance;
}
// Sending the distance to computer
Serial.print("Current distance: ");
Serial.println(distance);
Serial.print("Shortest distance: ");
Serial.println(shortestDistance);
Serial.println("");
//Delay for next reading.
delay(1000);
}

## Slide 16: Radar

## Slide 17: Radar
#include <Servo.h>
#define echo 11 // Echo Pin
#define trig 12 // Trigger Pin
Servo myServo;
int angle;
long travel_time, distance;
// Duration used to calculate distance
int shortestDistance=10000;
void setup() {
Serial.begin(9600);
pinMode(trig, OUTPUT);
pinMode(echo, INPUT);
myServo.attach(9);
}

## Slide 18: Radar
void loop() {
for (angle=0; angle<180; angle++){
myServo.write(angle);
delay(25);
digitalWrite(trig, LOW);
delayMicroseconds(2);
//Sending a high pulse to trigger the Ultrasound Module
digitalWrite(trig, HIGH);
delayMicroseconds(10);
digitalWrite(trig, LOW);
travel_time = pulseIn(echo, HIGH);
//Calculating the distance
distance = (travel_time*0.034)/2;
if (distance<shortestDistance){
shortestDistance = distance;
}
// Sending the distance to computer
Serial.print("Current distance: ");
Serial.println(distance);
Serial.print("Shortest distance: ");
Serial.println(shortestDistance);
Serial.println("");
//Delay for next reading.
delay(50);
}
for (angle=179; angle>0; angle--){
myServo.write(angle);
delay(25);
digitalWrite(trig, LOW);
delayMicroseconds(2);
//Sending a high pulse to trigger the Ultrasound Module
digitalWrite(trig, HIGH);
delayMicroseconds(10);

## Slide 19: Radar
digitalWrite(trig, LOW);
travel_time = pulseIn(echo, HIGH);
//Calculating the distance
distance = (travel_time*0.034)/2;
if (distance<shortestDistance){
shortestDistance = distance;
}
// Sending the distance to computer
Serial.print("Current distance: ");
Serial.println(distance);
Serial.print("Shortest distance: ");
Serial.println(shortestDistance);
Serial.println("");
//Delay for next reading.
delay(50);
}
}